## Slide 1: Production and Abatement of Non-Traditional Xenon Isotopes at a Spallation Neutron Source
Michael Foxe, Theodore Bowyer,
Matthew Cooper, James Ely,
Paul Eslinger, James Hayes,
Michael Mayer, Justin McIntyre, Mark Panisko
PNNL-SA-XXXXX
Release Statement: Cleared for release.
Notes: Stock image of cloud formations

## Slide 2: New Sources of Radioxenon
Anthropogenic sources of radioxenon are expanding
  Current Nuclear Reactors
  Medical Isotope Production
  Accelerator Facilities
    E.g., Spallation Neutron Source
  Advanced Nuclear Reactors
    E.g., Molten Salt Reactors
These new sources of radioxenon are also expanding the isotopes potentially detected at IMS stations

## Slide 3: Non-traditional Xenon Isotopes
Many isotopes can be produced via neutron irradiation
  127Xe
  125Xe
  129mXe
Neutron irradiation isotopes have been previously investigated and observed
122Xe produced as medical isotope via proton or alpha bombardment
  Not studied previously
McIntyre, Justin I et al.. 2008. “Generation of Radioxenon Isotopes.” In Proceedings of the 30th Seismic Research Review: Ground Based Nuclear Explosion Monitoring Technologies, 793–801.

## Slide 4: Xenon International
Next generation atmospheric radioxenon system
Faster and more sensitive than current generation systems
  ~2.5 cc of xenon in 6 hours
  Compared to ~1 cc for SAUNA II in 12 hours
MDCs
  <0.15 mBq/SCM for 133Xe, 131mXe, 133mXe
  <0.5 mBq/SCM for 135Xe
Developed at PNNL
  Transitioned to Teledyne Brown Engineering for production (Knoxville, TN)

## Slide 5: Puzzling Observations and Analyses - Measured at TBE in Knoxville, Tennessee
At initial glance, everything seems to be going well.
  133Xe – no unusual levels observed for the area
  135Xe – high but also not too unusual for the area
  133mXe – unusual to have higher concentration than 133Xe
  131mXe – similar concentration to 133mXe
Further investigation showed that the gamma-ray spectrum has unusual features.
133mXe
133Xe

## Slide 6: Atypical Coincidence Signatures - Measured at TBE in Knoxville, Tennessee
133mXe/133Xe
133Xe
135Xe
131mXe
Spectrum observed on Xenon International
Typical Xenon Signatures

## Slide 7: Monte Carlo Simulations
Monte Carlo simulations performed to observe clean signatures and extract efficiencies
Region at 511 keV in gamma energy not explained with these simulations
127Xe Simulation
129mXe Simulation
125Xe Simulation
Xenon International Measurement

## Slide 8: Missing Piece
122Xe simulation alone did not seem to generate missing signature
  Including daughter 122I (T1/2=3.63 minutes) produces missing signature
Only possible source of production of 122Xe is via spallation in the mercury target at Spallation Neutron Source (SNS)
122Xe Only Simulation
122Xe Full Decay Chain Simulation

## Slide 9: Correlation with SNS and HFIR Operation
Eslinger, Paul W. et al. 2022. “Determining the Source of Unusual Xenon Isotopes in Samples.” Journal of Environmental Radioactivity 247 (June): 106853. https://doi.org/10.1016/J.JENVRAD.2022.106853.
Counts
Radioxenon Data from 2020 not Associated with Traditional Radioxenon Isotopes

## Slide 10: Atmospheric Transport Modeling (ATM)
ATM suggests that likely release is from HFIR or SNS
Wind patterns are not consistent with release from the nuclear power plants
Production mechanism suggests
  SNS only
  SNS and HFIR
Publication on ATM
Eslinger, Paul W. et al. 2022. “Determining the Source of Unusual Xenon Isotopes in Samples.” Journal of Environmental Radioactivity 247 (June): 106853. https://doi.org/10.1016/J.JENVRAD.2022.106853.

## Slide 11: How is the Non-Traditional Radioxenon Produced?
Neutron bombardment of a liquid mercury target
  Trace amounts of uranium within the target
  Irradiation of natural xenon from air
Proton bombardment producing 122Xe
DeVore, Joe R, Lu, Wei, and Schwahn, Scott O. 2013. "NOBLE GAS PRODUCTION FROM MERCURY SPALLATION AT SNS". United States

## Slide 12: How is the radioxenon abated?
How much gets out of the target?
  Target material: liquid mercury
  Other sources use different target materials
What traps do the gases go through before being released?
  Helium off gases and purge for studying the production rates
  HEPA filters for particulate
  Cryogenic sulfur-impregnated charcoal absorber
How long is the xenon contained before being released?
  Initial retention time of approximately 350 minutes (1/3 122Xe half-life)
DeVore, Joe R, Lu, Wei, and Schwahn, Scott O. 2013. "NOBLE GAS PRODUCTION FROM MERCURY SPALLATION AT SNS". United States

## Slide 13: Other possible sources around the world
Neutron Activation Sources
  Accelerators
  Reactor cover gas
    Cover gas hold-up times impact the short-lived isotope interferences
Spallation sources
  SNS (this presentation)
  Los Alamos Neutron Science Center
  ISIS neutron source in the UK
  Japan Proton Accelerator Research Complex (J-PARC) in Japan
  European Spallation Source in Sweden
  China Spallation Neutron Source
Are there other commercial sources of these isotopes?

## Slide 14: Conclusion and Outlook
Newly observed isotopes seen near HFIR and SNS suggest new source of interfering xenon background (non-traditional production mechanisms)
New isotopes interfere with all traditional ROIs used for activity calculations
  Algorithms will continue to calculate normally
  Concentrations and ratios will not make sense
Non-traditional xenon isotopes are produced through a series of mechanisms
  Spallation on mercury targets
  Air activation
  Fission isotopes
Even with wind predominantly in the other direction, they can still be detected at near-by stations
These non-traditional isotopes may be produced at other facilities around the world